## Slide 1
OpenCRG Workshop
Topic: Additional Data Layers
Dec 05, 2019
Marius Dupuis
Managing Director
VIRES Simulationstechnologie GmbH

## Slide 2
Requirements
Definition
Evaluation
Data layers shall be clearly identifiable in the header section
Reference line shall be valid for all data layers
Longitudinal and Lateral grid shall apply to all data layers
Data layers shall have scalable grid resolution vs. basic grid
Options and Modifiers shall be applicable per layer
Files shall be self-contained, i.e. layers must not be spread across multiple files
Layers shall be treated as data sets (internal detail…)
Evaluation of all layers or selected layers only shall be feasible

## Slide 3
Layer n Data
Layer 1 Data
Layer n Modifiers
Layer n Options
Layer 1 Modifiers
Layer 1 Options
Layer Defs.
Reference
Global Modifiers
Global Options
File Structure
Data
Reference
Modifiers
Options
Channel Defs.
Road Def.
Comment
TODAY
$CT: mandatory comment about file's contents
$ROAD_CRG: information about centerline;
$KD_Definition: definition of individual channel parameters
$ROAD_CRG_OPTS: evaluation options
$ROAD_CRG_MODS: data set modifiers
$ROAD_CRG_FILE: references to other data files
the actual OpenCRG® data
TOMORROW
Channel Defs.
Road Def.
Comment
$CT
$ROAD_CRG
$KD_Definition
$ROAD_CRG_OPTS
$ROAD_CRG_MODS
$ROAD_CRG_FILE
$LAYERS
$LAYER_OPTS
$LAYER_MODS
:
$LAYER_OPTS $LAYER_MODS
actual data of layer 1
:
actual data of layer n
NOTE:
  Where no LAYER definition block is present, the file corresponds to the established OpenCRG file format.

## Slide 4
File Header
$LAYERS
  $LAYER
    LAYER_ID = [0..n]
    LAYER_NAME = [text]
    LAYER_PURPOSE = [text]
    LAYER_RESOLUTION_U = [1..n]
    LAYER_RESOLUTION_V = [1..n]
    LAYER_ACTIVE = [0/1]
    LAYER_HAS_PHI = [0/1]
  $LAYER
  :
TAGS
$LAYER_OPTS
  $LAYER
    LAYER_ID = [0..n]
    BORDER_MODE_U = [0..4]
    BORDER_MODE_V = [0..4]
    BORDER_OFFSET_U = [float]
    BORDER_OFFSET_V = [float]
  $LAYER
  :
$LAYER_MODS
  $LAYER
    LAYER_ID = [0..n]
    SCALE_Z = [float]
    GRID_NAN_MODE = [0..2]
    GRID_NAN_OFFSET = [float]
  $LAYER
  :

## Slide 5
Implementation - Definitions
$LAYERS
  $LAYER
    LAYER_ID = [0..n]
    LAYER_NAME = [text]
    LAYER_PURPOSE = [text]
    LAYER_RESOLUTION_U = [1..n]
    LAYER_RESOLUTION_V = [1..n]
    LAYER_ACTIVE = [0/1]
  $LAYER
  :
FILE TAGS
crgLayerSetName( dataSetId, layer, name );
crgLayerSetPurpose( dataSetId, layer, purpose );
crgLayerSetActive( dataSetId, layer, active );
C-API
Mandatory tags are in bold font.

## Slide 6
  LAYER_PURPOSE = [ "default" | "phi" | „elevation" | "friction" | "temperature" | "custom" ]
CONSTANTS
there shall be exactly one active layer providing phi (either isolated or in combination with scalar)
there shall be at least one active layer
there shall be at least one layer at full resolution_u (i.e. factor = 1); this might even just be the phi layer
the layer providing phi shall be at full resolution_u
there shall be only one active layer per purpose (exception: purpose custom)
  LAYER_PURPOSE = "default"
  LAYER_NAME = „unknown"
  LAYER_RESOLUTION_U = 1
  LAYER_RESOLUTION_V = 1
  LAYER_ACTIVE = 1
  LAYER_HAS_PHI = 1
DEFAULTS
CHECKS
NOTE:
  the layer purpose „default“ represents the „classic“ OpenCRG data file
  The layer purpose „custom“ requires an additional tag
    LAYER_CUSTOM_PURPOSE = [name]
Implementation - Definitions

## Slide 7
Implementation – Loading and Queries
unsigned int dataSetId = crgLoaderReadFile( filename ) );
unsigned int nLayers = crgDataSetGetNoLayers( dataSetId );
for ( unsigned int i = 0; i < nLayers; i++ )
{
crgLayerGetId( dataSetId, i );
crgLayerGetName( dataSetId, i );
crgLayerGetPurpose( dataSetId, i );
crgLayerGetResolutionU( dataSetId, i );
crgLayerGetResolutionV( dataSetId, i );
crgLayerIsActive( dataSetId, i );
crgLayerHasPhi( dataSetId, i );
}
crgDataSetGetLayerByName( dataSetId, name );
crgDataSetGetLayerByPurpose( dataSetId, purpose );
crgGetLayerByName( cpId, name );
crgGetLayerByPurpose( cpId, purpose );
GOAL
Keep changes to API calls and implementations at a minimum
Introduce a „lean“ management level for layer handling

## Slide 8
Implementation – Example
unsigned int dataSetId = crgLoaderReadFile( filename ) );
unsigned int noLayers = crgDataSetGetNoLayers( dataSetId );
unsigned int cpId = crgContactPointCreate( dataSetId );
double u, v, value;
crgEvalxy2uv( cpId, x, y, &u, &v ); // compute u/v only once and apply multiple times
for ( unsigned int i = 0; i < nLayers; i++ ) {
crgUseLayer( cpId, i );
crguv2z( cpId, u, v, &value );
:
}
Query all layers
or
double *valueArray;
unsigned int nValues;
crguv2zArray( cpId, u, v, &valueArray, &nValues );
:
free( valueArray );

## Slide 9
Implementation – Example
int layerId = crgGetLayerByPurpose( cpId, dCrgLayerPurposeFriction );
crgUseLayer( cpId, layerId );
crguv2z( cpId, u, v, &value );
Find and query a single layer
int layerId = crgDataSetGetLayerByPurpose( dataSetId, dCrgLayerPurposeFriction );
crgUseLayer( cpId, layerId );
crguv2z( cpId, u, v, &value );
or
unsigned int dataSetId = crgLoaderReadFile( filename ) );
unsigned int noLayers = crgDataSetGetNoLayers( dataSetId );
unsigned int cpId = crgContactPointCreate( dataSetId );
double u, v, value;
crgEvalxy2uv( cpId, x, y, &u, &v ); // compute u/v only once and apply multiple times

## Slide 10
Documentation
Specification of data format with
  new keywords for layers
  data arrangement rules
C-API
Implementation – Next Steps
MATLAB API
User Manual
Implementation
  Add symbolic constants
  Modify data structures
  Update loader methods
  Add layer operation methods
  Modify checker
    Data integrity per layer
    Reference line
    Layer activity
  Modify contact point history
Tests
  Define layer-centric tests
  Create text-based sample files
  Conduct tests on sample files
  Measure performance vs. current implementation
  Conduct tests on binary sample files
C-API documentation
Implementation
  Modify data structures
  Update loader methods
  Add layer operation methods
    addLayer
    removeLayer
    shiftLayer
    extractLayer
    setLayerAttribute
  Modify checker
    Data integrity per layer
    Reference line
  Extend all existing methods with a layer identifier
Tests
  Define layer-centric tests
  Create text and binary sample files
Matlab documentation

## Slide 11
Documentation
Specification of data format with
  new keywords for layers
  data arrangement rules
C-API
Implementation – Next Steps –
MATLAB API
User Manual
  Gfx provided by implementation provider (from tests)
  Reformatting / rewriting / extending
Implementation
  Add symbolic constants
  Modify data structures
  Update loader methods
  Add layer operation methods
  Modify checker
    Data integrity per layer
    Reference line
    Layer activity
  Modify contact point history
Tests
  Define layer-centric tests
  Create text-based sample files
  Conduct tests on sample files
  Measure performance vs. current implementation
  Create documentation assets
  Conduct tests on binary sample files
C-API documentation
Implementation
  Modify data structures
  Update loader methods
  Add layer operation methods
    addLayer
    removeLayer
    shiftLayer
    extractLayer
    setLayerAttribute
    tbd.
  Modify checker
    Data integrity per layer
    Reference line
  Extend all existing methods with a layer identifier
Tests
  Define layer-centric tests
  Create text and binary sample files
  Create documentation assets
Matlab documentation

## Slide 12
Thank You.